## Slide 1: Base Load Measures
WEATHERIZATION ENERGY AUDITOR SINGLE FAMILY
GJA 2024 Version III
1

## Slide 2: Learning Objectives
By attending this session participants will:
Learn the definition of base load measures.
Recognize base load measures allowable in the WAP based on Appendix A.
Understand how to use utility bill analysis to determine base load usage.
Be introduced to tools useful for calculating energy and money savings associated with common base load measures.
GJA 2024 Version III
2
Notes: By attending this session, participants will:
Learn the definition of base load measures.
Recognize base load measures allowable in the WAP based on Appendix A.
Understand how to use utility bill analysis to determine base load usage.
Be introduced to tools useful for calculating energy and money savings associated with common base load measures.

## Slide 3: Base Load Defined
Base Load:
The energy used by electric or gas appliances in a home that is not used for space conditioning, thus not a seasonal load.
Typical Measures include:
Lighting Retrofits – upgrade to LED
Replace inefficient refrigerators, window air conditioners, electric water heaters
Water Conservation: low-flow showerheads and aerators, clothes washers
Base Load Measures
GJA 2024 Version III
3
Notes: Base load: The energy used by electric or gas appliances in a home that is not used for space conditioning, and therefore is not a seasonal load.
Typical measures include:
Lighting retrofits – Replacing incandescent or halogen bulbs with compact fluorescent lamps (CFLs).
Refrigerator replacement.
Water heater modification.
Installation of low-flow fixtures, such as low-flow showerheads and faucet aerators.

## Slide 4: Why Target Electric Base Loads?
Source: Energy Information Administration, U.S. Department of Energy
30% Space Heating
5% Cooking/Dryer
15% Water Heating
Space Cooling 9%
Appliances 26% (other) ….
Refrigerator 9%
Lighting 6%
Energy Cost Breakdown in income-eligible households
Base Load Measures
50% Electric
50% Fossil Fuel
GJA 2024 Version III
4
Notes: Graph: Percent of Total Energy End Use of Income Eligible Households.
Space heating and cooling make up 39% of the energy use in weatherization-eligible homes. That means 61% of the total energy use is base load and can be reduced by modifying or replacing existing appliances to increase efficiency.

## Slide 5: Why Target Electric Base Loads?
In households with Electric Heat, base loads account for about half of the total energy use.
In many homes heated with fossil fuels, the total annual electric bills are higher than the total fuel bills.
Base Load Measures
GJA 2024 Version III
5
Notes: About half of the electricity used by households with electric heat is for base loads.
Many houses heated with fossil fuel have higher annual electric bills than gas or oil bills.

## Slide 6: Consumption Analysis
1. Bill Analysis
2. Site Survey
3. Reconcile the Two
GJA 2024 Version III
6
Notes: Consumption analysis includes three steps:
Bill analysis – How much energy is going to base load uses?
Site survey – What are the main base loads?
Reconciliation of the two – Do the utility bills make sense in light of the site survey?

## Slide 7: Simple Bill Analysis Method
Estimating the Annual Base Load Consumption
Review the previous 12 months.
Average the three lowest months.
Multiply by 12.
GJA 2024 Version III
7
Notes: Review the previous 12 months of the client’s energy bills. This reveals seasonal loads associated with heating and cooling.
Average the three lowest months, which are those with little-to-no heating or cooling costs. These months provide a picture of the total base load of the home. Averaging the three months together helps to account for vacations when the home was empty or high-use weeks that are out of the ordinary.
Multiply by 12 to estimate annual base load usage.

## Slide 8: Site Survey Analysis
Site Survey Analysis
Account for typical consumption.
  Where does all the juice go?
Build a consumption table based on:
  Client interviews.
  Known and guesstimated wattages.
Hint – Identify the 5 biggest users.
GJA 2024 Version III
8
Notes: Account for typical consumption.
  Where does all the juice go?
Build a consumption table based on client interviews and known and guesstimated wattages.
Hint – Identify the five biggest users.
Ask trainees what they think are typically the five biggest users.
They are lighting, hot water heaters, refrigerators, clothes driers, and various electronics (especially flat-screened TVs).

## Slide 9: Post-Survey Analysis
Post-Survey Analysis
Are there existing loads where consumption can be reduced by:
  Repairing?
  Replacing?
  Client education?
Is it cost effective?
GJA 2024 Version III
9
Notes: After analyzing consumption, the question becomes whether the WAP can lower base load energy use for this home.
Are there existing loads whose consumption can be reduced by:
  Repair?
Installation or replacement?
Client education?
Is it cost-effective? Except for health and safety measures, all measures installed with WAP money must be cost-effective.

## Slide 10: Bill Analysis: Example #1
Date | # of Days | Reading | kWh
5/7/99 | 29 | 06248 | 1031
4/8/99 | 30 | 05217 | 1968
3/9/99 | 29 | 03249 | 3143
2/8/99 | 31 | 00106 | 3356
1/8/99 | 32 | 96750 | 3648
12/7/98 | 33 | 93102 | 2206
11/4/98 | 29 | 90896 | 1327
10/6/98 | 32 | 86569 | 576
9/4/98 | 29 | 88993 | 442
8/6/98 | 29 | 88551 | 874
7/8/98 | 30 | 87667 | 522
6/8/98 | 32 | 87155 | 538
5/7/98 | 30 | 86617 | 941
GJA 2024 Version III
10
Notes: This table is typical of the information utility companies will provide. For bill analysis, the critical facts are:
Month.
Amount of kWh used that month.
Q. Based on the information shown here, is this sample home in a heating-dominated or cooling-dominated climate?
A. Heating-dominated. The highest-use months are in the winter: January, February, and March, indicating electric heating in a cold climate.

## Slide 11: Bill Analysis: Example #1
Month | Bill kWh | Ave. Base Load | Heat? | Cool?
Jan | 3,356 |  |  | 
Feb | 3,143 |  |  | 
Mar | 1,968 |  |  | 
Apr | 1,031 |  |  | 
May | 538 |  |  | 
June | 522 |  |  | 
July | 874 |  |  | 
Aug | 442 |  |  | 
Sept | 576 |  |  | 
Oct | 1,327 |  |  | 
Nov | 2,206 |  |  | 
Dec | 3,648 |  |  | 
Total | 19,631 |  |  | 
% Base Load Use |  |  |  | 
Lowest Reading | 
2nd Lowest | 
3rd Lowest | 
Average Monthly Base Load | 
442
522
538
1,502/3
= 501
GJA 2024 Version III
11
Notes: Here is that same information, inserted into the bill analysis table.
Q. Which are the three lowest months for energy use?
A. Click to reveal the three lowest readings, from August, June, and May, and the average monthly base load calculation.
In this example, approximately 501 kWh/month are used for base load.

## Slide 12: Bill Analysis: Example #1
Month | Bill kWh | Ave. Base Load | Heat? | Cool?
Jan | 3,356 | 501 |  | 
Feb | 3,143 | 501 |  | 
Mar | 1,968 | 501 |  | 
Apr | 1,031 | 501 |  | 
May | 538 | 501 |  | 
June | 522 | 501 |  | 
July | 874 | 501 |  | 
Aug | 442 | 501 |  | 
Sept | 576 | 501 |  | 
Oct | 1,327 | 501 |  | 
Nov | 2,206 | 501 |  | 
Dec | 3,648 | 501 |  | 
Total | 19,631 | 6,008 |  | 
% Base Load Use |  | 31% |  | 
Lowest Reading | 442
2nd Lowest | 522
3rd Lowest | 538
Average Monthly Base Load | 501
GJA 2024 Version III
12
Notes: Click to highlight the annual percentage of the energy bill that is base load.
501 kWh makes up 31% of this home’s total energy bill.

## Slide 13: Bill Analysis: Example #1
Month | Bill kWh | Ave. Base Load | Heating? | Cooling?
Jan | 3,356 | 501 | 2,855 | 
Feb | 3,143 | 501 | 2,642 | 
Mar | 1,968 | 501 | 1,467 | 
Apr | 1,031 | 501 |  | 
May | 538 | 501 |  | 
June | 522 | 501 |  | 21
July | 874 | 501 |  | 373
Aug | 442 | 501 |  | -59
Sept | 576 | 501 |  | 
Oct | 1,327 | 501 |  | 
Nov | 2,206 | 501 | 1,705 | 
Dec | 3,648 | 501 | 3,147 | 
Total | 19,631 | 6,008 |  | 
% Base Load Use |  | 31% |  | 
Lowest Reading | 442
2nd Lowest | 522
3rd Lowest | 538
Average Monthly Base Load | 501
GJA 2024 Version III
13
Notes: The remaining 69% can then be separated into suspected heating and cooling loads.

## Slide 14: Bill Analysis: Example #2
Date | # of Days | Reading | kWh
1/29/99 | 30 | 65389 | 344
12/30/98 | 35 | 65045 | 418
11/25/98 | 29 | 64627 | 347
10/27/98 | 29 | 64280 | 330
9/28/98 | 32 | 63950 | 422
8/27/98 | 28 | 63528 | 401
7/30/98 | 30 | 63127 | 416
6/30/98 | 32 | 62711 | 455
5/29/98 | 30 | 62256 | 390
4/29/98 | 30 | 61866 | 312
3/30/98 | 28 | 61554 | 262
3/2/98 | 32 | 61292 | 255
1/29/98 | 30 | 61037 | 312
GJA 2024 Version III
14
Notes: Another bill analysis example.
Q. Based on the information shown here, is this a heating- or cooling-dominated climate?
A. It’s difficult to say for sure, but it looks like either a very moderate climate, or the home uses alternative fuel for heating since there is very little fluctuation in seasonal energy usage.

## Slide 15: Bill Analysis: Example #2
Month | Bill kWh | Ave. Base Load | Heat? | Cool?
Jan | 344 |  |  | 
Feb | 255 |  |  | 
Mar | 262 |  |  | 
Apr | 312 |  |  | 
May | 390 |  |  | 
June | 455 |  |  | 
July | 416 |  |  | 
Aug | 401 |  |  | 
Sept | 422 |  |  | 
Oct | 330 |  |  | 
Nov | 347 |  |  | 
Dec | 418 |  |  | 
Total | 4,352 |  |  | 
% Base Load Use |  |  |  | 
Lowest Reading | 
2nd Lowest | 
3rd Lowest | 
Average Monthly Base Load | 
255
262
312
829/3
= 276
GJA 2024 Version III
15
Notes: Q. Which are the three lowest months for energy use?
A. Click to reveal the three lowest readings, from February, March, and April, and the average monthly base load calculation.

## Slide 16: Bill Analysis: Example #2
Month | Bill kWh | Ave. Base Load | Heat? | Cool?
Jan | 344 | 276 |  | 
Feb | 255 | 276 |  | 
Mar | 262 | 276 |  | 
Apr | 312 | 276 |  | 
May | 390 | 276 |  | 
June | 455 | 276 |  | 
July | 416 | 276 |  | 
Aug | 401 | 276 |  | 
Sept | 422 | 276 |  | 
Oct | 330 | 276 |  | 
Nov | 347 | 276 |  | 
Dec | 418 | 276 |  | 
Total | 4,352 | 3,316 |  | 
% Base Load Use |  | 76% |  | 
Lowest Reading | 255
2nd Lowest | 262
3rd Lowest | 312
Average Monthly Base Load | 276
GJA 2024 Version III
16
Notes: This home uses far less energy overall, and only a little over half the energy the previous home used for base load, but base load makes up a whopping 76% of the annual energy bill.
Click to highlight the annual percentage of the energy bill that is base load.

## Slide 17: Bill Analysis: Example #3
Date | # of Days | Reading | kWh
2/24/00 | 29 | 10036 | 1904
1/26/00 | 30 | 08132 | 2097
12/27/99 | 40 | 06035 | 2341
11/17/99 | 30 | 03694 | 1382
10/18/99 | 31 | 02312 | 695
9/17/99 | 30 | 01617 | 1334
8/18/99 | 28 | 00283 | 1175
7/21/99 | 34 | 99108 | 1314
6/17/99 | 29 | 97794 | 888
5/19/99 | 28 | 96906 | 752
4/21/99 | 30 | 96154 | 1182
3/22/99 | 29 | 94972 | 1826
GJA 2024 Version III
17
Notes: Here’s one last bill analysis example.
Q. Based on the information shown here, is this a heating- or cooling-dominated climate?
A. Heating-dominated. The highest-use months are in the winter.

## Slide 18: Bill Analysis: Example #3
Month | Bill kWh | Ave. Base Load | Heat? | Cool?
Jan | 2,097 |  |  | 
Feb | 1,904 |  |  | 
Mar | 1,826 |  |  | 
Apr | 1,182 |  |  | 
May | 752 |  |  | 
June | 888 |  |  | 
July | 1,314 |  |  | 
Aug | 1,175 |  |  | 
Sept | 1,314 |  |  | 
Oct | 695 |  |  | 
Nov | 1,382 |  |  | 
Dec | 2,341 |  |  | 
Total | 16,870 |  |  | 
% Base Load Use |  |  |  | 
Lowest Reading | 
2nd Lowest | 
3rd Lowest | 
Average Monthly Base Load | 
2,335/3
= 778
695
752
888
GJA 2024 Version III
18
Notes: Once again, averaging the three lowest readings provides us with the average monthly base load: 778 kWh.
Click to reveal the three lowest readings and calculations.

## Slide 19: Bill Analysis: Example #3
Month | Bill kWh | Ave. Base Load | Heat? | Cool?
Jan | 2,097 | 778 |  | 
Feb | 1,904 | 778 |  | 
Mar | 1,826 | 778 |  | 
Apr | 1,182 | 778 |  | 
May | 752 | 778 |  | 
June | 888 | 778 |  | 
July | 1,314 | 778 |  | 
Aug | 1,175 | 778 |  | 
Sept | 1,314 | 778 |  | 
Oct | 695 | 778 |  | 
Nov | 1,382 | 778 |  | 
Dec | 2,341 | 778 |  | 
Total | 16,870 | 9,340 |  | 
% Base Load Use |  | 55% |  | 
Lowest Reading | 695
2nd Lowest | 752
3rd Lowest | 888
Average Monthly Base Load | 778
GJA 2024 Version III
19
Notes: At an average of 778 kWh/month, base load accounts for 55% of this home’s annual energy use.
Click to highlight the annual percentage of the energy bill that is base load.

## Slide 20: Bill Analysis: Example #3
Month | Bill kWh | Ave. Base Load | Heat? | Cool?
Jan | 2,097 | 778 | 1,319 | 
Feb | 1,904 | 778 | 1,126 | 
Mar | 1,826 | 778 | 1,048 | 
Apr | 1,182 | 778 |  | 
May | 752 | 778 |  | 
June | 888 | 778 |  | 110
July | 1,314 | 778 |  | 536
Aug | 1,175 | 778 |  | 397
Sept | 1,314 | 778 |  | 
Oct | 695 | 778 |  | 
Nov | 1,382 | 778 | 604 | 
Dec | 2,341 | 778 | 1,563 | 
Total | 16,870 | 9,340 |  | 
% Base Load Use |  | 55% |  | 
Lowest Reading | 695
2nd Lowest | 752
3rd Lowest | 888
Average Monthly Base Load | 778
GJA 2024 Version III
20
Notes: The remaining 45% can then be separated into suspected heating and cooling loads.

## Slide 21: What is High Usage?
The greater the waste, the greater potential for savings.
Publications showing kWh consumption estimates for appliances often differ.
Sources: government agencies and research centers such as DOE EnergyStar, utility companies, and trade groups like the American Home Appliance Manufacturers (AHAM).
Conducting on-site metering using a watt-meter measures kilowatt hour consumption over an elapsed time.
Base Load Measures
GJA 2024 Version III
21
Notes: The greater the waste, the greater potential for savings.
Charts and table from experts, utilities, etc. seldom agree on the exact kWh for average or high usage of appliances.

## Slide 22: Appliance Energy Use (Annual)
Appliance | Low kWh | Mid kWh | High kWh
Refrigerator | 400 | 900 | 1,500
Clothes Dryer | 500 | 900 | 1,200
Clothes Washer | 500 | 900 | 1,200
Indoor Lighting | 350 | 900 | 1,200
Air Conditioning | 300 | 500 | 750
Cooking | 300 | 500 | 750
Television | 200 | 350 | 600
Outdoor Lighting | 50 | 250 | 350
Space Heating Motors | 150 | 250 | 350
Stereo | 100 | 200 | 300
Hair Dryer | 25 | 100 | 200
Vacuum Cleaner | 25 | 50 | 75
Miscellaneous | 100 | 200 | 400
Base Load Measures
GJA 2024 Version III
22
Notes: This table shows the wide range of energy use within a single class of appliances.
Many factors affect the energy efficiency of appliances including:
Age – Most appliances decline in efficiency each year they operate.
Standards – Federal efficiency standards at the time of manufacture regulate the unit’s maximum energy use.
Size – Bigger may mean better to some, but it generally means more energy use.
Special features – Through-the-door ice and water service on refrigerators ups energy usage significantly. Moisture-sensors on clothes dryers reduce energy use.
User habits – Leaving lights on, standing in front of an open refrigerator deciding what to eat, and running air conditioners with the windows open are all example of user habits that increase energy use.

## Slide 23: (Very) General Rule of Thumb
There may be good potential for savings if a 4-person household uses:
More than 600 kWh/month without an electric water heater, or
More than 1,000 kWh/month with an electric water heater.
Base Load Measures
GJA 2024 Version III
23
Notes: There may be good potential for savings if a 4-person household uses:
More than 600 kWh/month without an electric water heater.
More than 1,000 kWh/month with an electric water heater.

## Slide 24: Occupant Impacts
Base load is affected by:
  Number of occupants, pets & aquariums
  Size and efficiency of equipment.
  Habits of occupants.
Client education is the key to effectively reducing base load energy use.
GJA 2024 Version III
24
Notes: Base load use is affected by:
The number of occupants.
Size and efficiency of the equipment.
Habits of occupants.
In many cases, appliances may not qualify for replacement, but clients can still reduce their energy use by changing habits. Client education is key.

## Slide 25: Lighting
Lighting accounts for up to 10% of total home energy use.
Compact Fluorescent Lighting reduced it to about 4%.
LED lighting reduced it to about 2%.
GJA 2024 Version III
25
Notes: Lighting accounts for up to 10% of total home energy use.
CFL retrofits can cut lighting energy use by 75%, yielding an overall energy reduction of 7.5% for the home.

## Slide 26: Lumen Table
  CFLs save energy by producing more light (output) per watt of energy used.
  The light output is measured in lumens.
Incandescent (watts) | Minimum Light Output (lumens) | Common ENERGY STAR Qualified Bulbs (watts)
40 | 450 | 9 to 13
60 | 800 | 13 to 15
75 | 1,100 | 18 to 25
100 | 1,600 | 23 to 30
150 | 2,600 | 30 to 52
Base Load Measures
GJA 2024 Version III
26
Notes: Table showing wattage of incandescent bulbs and CFLs with comparable lumen output
CFLs save energy by producing more light per watt of energy used.
The light output is measured in lumens.

## Slide 27: Lighting Savings Table
CFLs save energy by producing more light output (measured in lumens) per watt of energy used.
Incandescent (watts) | Average Usage (Hrs/Day) | CFL Replacement (watts) | Annual Savings* ($/ bulb replaced)
40 | 4 | 9 - 13 | 4.98
60 | 4 | 13 - 15 | 7.55
75 | 4 | 18 - 25 | 9.15
100 | 4 | 23 - 30 | 12.37
150 | 4 | 30 - 52 | 19.27
* Annual Savings based on $0.11/kWh.
Base Load Measures
GJA 2024 Version III
27
Notes: Table showing annual savings per bulb for a range of CFL replacements
The greater the use, the greater the potential savings.
These numbers are based on $0.11/kWh.
This table shows just one year of savings and does not account for the costs associated with replacing incandescent bulbs, which burn out about 10 times faster than CFLs.

## Slide 28: Lighting & CFL Considerations
Dimmers
Photocells
Specialty bulbs (candelabra, recessed, exterior, etc.)
Color Scale
  CRI: 0 – 100; most CFLs are between 80-90
  Kelvin Temperature
    2700 - 3000K: Warm white/Soft white light (incandescent)
    3500 - 4100K: Cool or Bright White light
    5000 - 6500K: Natural or Daylight
Base Load Measures
GJA 2024 Version III
28
Notes: Some people may be reluctant to have CFLs installed in their homes due to past experiences or sensationalized news stories about the mercury content. Specify these replacements to ensure that clients have positive experiences with their lighting retrofits:
Dimmers – General-use CFLs are not designed to work with dimmer switches. Special CFLs are available. Be sure to specify “dimmer compatible” CFLs when replacing incandescent bulbs in fixtures with dimmer switches.
Photocells – General-use CFLs are not designed to work with photocells. Dimmer-compatible bulbs do work in these fixtures.
Specialty bulbs (candelabra, reflectors, etc.) – Specify a replacement that fits the fixture properly, accepting whatever lampshade or other hardware is part of the fixture.
Color scale – One of the most common complaints about CFLs is that the light is unflattering. Avoid this problem by specifying bulbs according to the color scale.
  CRI: 0–100; most CFLs are between 80 and 90.
Kelvin temperature.
    2700–3000K: Warm white/soft white light.
3500–4100K: Cool or bright white light.
5000–6500K: Natural or daylight.
Mercury – There is a small amount of mercury in each bulb. How small?
Ask students if they have heard concerns about mercury in CFLs.

## Slide 29: Refrigerator Replacement
Replacement includes removal and decommissioning of old unit, must be included in cost for SIR calculations.
Only when cost-effective, SIR ≥ 1.
Based on metering or recognized database (AHAM, Home Energy, or Weatherization Refrigerator Guide).
Must meter at least 10% of units.
GJA 2024 Version III
29
Notes: Replacement includes removal and decommissioning of the old unit to ensure it will not be plugged in again. Decommissioning includes removal, proper storage of refrigerants, and ideally, recycling of the refrigerator. All these expenses must be included in the cost for SIR calculations.
Refrigerator replacement is allowed only when it is cost-effective, i.e., SIR ≥ 1.
Energy usage of the existing appliance is based on metering or data from a recognized database (AHAM, Home Energy, or WAP Refrigerator Guide) corrected for temperature and other factors.
You must meter at least 10% of units, even if all units can be found in the database.

## Slide 30: Refrigerator Replacement
Typically the best ECM. Bigger motor than other base load appliances. Usually runs about 6 hours/day.
Older models are typically energy hogs.
Worn gaskets make the unit run more often.
Can guess insulation by pushing on door.
  - Pushes in easily – likely fiberglass
  - Does not – likely solid foam
  - Door thickness
GJA 2024 Version III
30
Notes: Older models are typically energy hogs.
Worn gaskets make the unit run more often.
You can guess the type of insulation by pushing on the door.
  If it pushes in easily, it is likely fiberglass and less efficient.
If it does not push in easily, it is likely solid foam and more efficient.
If Coppertone brown, avocado green, or harvest gold, replacements can be cost-effective. These colors were popular before current efficiency guidelines, and typically indicate an older model.

## Slide 31: Michael Blasnik’s Refrigerator Study
In the Northeast, add 10% to DOE rating.
Other factors affect actual use:
  Occupants: add 5% per occupant
  Anti-sweat switch on: add 20%
  Through-the-door ice service: add 15%
  Visible gaps in door seal: add 15%
  Refrigerator bought used: add 20%
  Thermostat setting high: add 5%
  Thermostat setting really high: add 10%
Refrigerators in basements or garages should be metered.
Base Load Measures
GJA 2024 Version III
31
Notes: Findings from this study have not yet been replicated in other regions or formally adopted into WAP procedures, but they can help auditors more accurately predict energy usage of refrigerators based on approved databases. If relying on a database for usage, applying these corrections presents a more accurate picture of how much energy is being consumed. These corrections may help qualify units that will provide positive energy savings, but wouldn’t have qualified based solely on the less accurate database figures.
From June 2003 to May 2004, researchers monitored electricity usage and room temperature for two weeks of 160 existing units and 30 Energy Star qualified replacement units.
In the Northeast, adding 11% to the DOE rating is a fairly good predictor of actual use if the unit is located in the living space (i.e., not in the unconditioned basement).
Other factors affect actual use. The following table summarizes the survey results:
Factors Affecting Refrigerator Usage & Proposed New Audit Approach1
Factor Proposed Audit Approach Notes
Number of occupants Add 5% per occupant to rated use Only for primary refrigerators.
Anti-sweat switch on Add 20% to rated use Expect ~ 15% higher.
Through-the-door ice service Add 15% to rated use Captures side-by-side effect.
Visible gaps in door seal Add 15% to rated use Related to continuous running.
Refrigerator bought used Add 20% to rated use Related to continuous running.
Average room temperature Add 5% to rated use if the Annual temperature effects can be Subtract 5% from rated use if the roughly accounted for by adjusting average winter temperature in low/ usage up or down if average winter mid-60’s thermostat settings are outside the typical range of 65°-70°F.
Base level usage 85% Usage estimates if there are no occupants or TTD ice, the anti-sweat switch is not on, door seals are in good condition, the unit was bought new or came with the house, and winter thermostat settings are typical.
1Blasnik, Michael. Measurement and Verification of Residential Refrigerator Energy Use: Final Report: 2003-2004 Metering Study. 2004.

## Slide 32: Metering
At least 2 hours.
Disable defrost cycle for duration.
Adjust for temperature variation.
Base Load Measures
GJA 2024 Version III
32
Notes: These are the formal rules for metering refrigerators:
Meter for at least 2 hours.
Disable the defrost cycle for the duration of the test.
Adjust for temperature variation.

## Slide 33: Metering Duration ≥ 2 Hours
Debate over how long a refrigerator must be metered to precisely estimate annual energy use.
Less than 2 of 10 one-hour tests were accurate within ±10%
But 9 of 10 three-hour tests were accurate ±10%.
Currently recommending at least 2 hours.
GJA 2024 Version III
33
Notes: There is debate over how long a refrigerator must be metered to accurately estimate annual energy use.
One-hour tests are accurate within ±10% only 18 times out of 100.
Three-hour tests increase that accuracy to 90 times out of 100.
WAP currently recommends metering for at least 2 hours.

## Slide 34: Defrost Cycles
Defrost cycles during metering can significantly affect accuracy of results.
Demand of 380 watts or more usually indicates the defrost heaters are on.
If no defrost cycle during metering, add 8% to metering results.
Base Load Measures
GJA 2024 Version III
34
Notes: Defrost cycles during metering can significantly affect the accuracy of results.
Demand of 380 watts or more usually indicates the defrost heaters are on.
If there is no defrost cycle during metering, add 8% to the metering results to account for the annual additional energy use due to the defrost cycle.

## Slide 35: Defrost Timers
Figure Source: Refrigerator Guide
Square / Rectangular Timers
Typical Timers
GJA 2024 Version III
35
Notes: To prepare for metering the refrigerator, advance the defrost timer through the defrost cycle. Metering should begin at the start of a “fresh” cycle with no risk of the defrost kicking in during the metering period.
The Refrigerator Info Toolkit on www.waptac.org and on the curriculum CD contains all of this information.

## Slide 36: Defrost Timer Locations
Timer may be found in virtually the same locations in top- or bottom-freezer models or side-by-sides.
May be behind lighting panel
May be under a small panel in the roof of the food compartment
Timer may be located inside the FREEZER section of certain bottom-freezer models.
Usually inside of a removable mounting box
Most common place is somewhere behind the kickplate. (Shown removed in this illustration.) You may need to lift or move a bundle of wires to see it.
Figure Source: Refrigerator Guide
GJA 2024 Version III
36
Notes: These are the common places to look for the defrost timer:
Behind the kickplate (most common).
Behind the lighting panel.
Inside the freezer of certain bottom-freezer models.
On the rear of the refrigerator in a removable mounting box (less common).
This is also included in the toolkit.

## Slide 37: Advancing Defrost Timers
Use a broad-tipped screwdriver to advance past the defrost cycle for metering purposes.
Remember to add 8% to metered results to account for regular defrost cycles.
Some timers have a defrost cycle every 180 degrees; in others, it’s every 360 degrees.
1st Loud Click
2nd Loud Click
Run Cycle
Defrost Cycle
Figure Source: Refrigerator Guide
Base Load Measures
GJA 2024 Version III
37
Notes: Use a broad-tipped screwdriver to advance past the defrost cycle for metering purposes.
Some timers have a defrost cycle every 180 degrees. In others, it’s every 360 degrees.
Remember to add 8% to metered results to account for regular defrost cycles.

## Slide 38: Adjust for Temperature Variation
DeltaT between inside the refrigerator and ambient effects efficiency: 2.25% to 2.5% per °F.
To calculate correction factor, multiply the temperature difference by 2.5%.
If kitchen is cooler than normal during metering, add the correction. If warmer, subtract.
For example, if the kitchen is normally 72°F, but the temperature is 66°F during metering:
1+ (2.5% x (72°F - 66°F)) = 1+ (0.025 x 6) = 1.15
GJA 2024 Version III
38
Notes: After metering, the auditor must apply corrections to account for temperature variations. If the unit is metered on an uncommonly hot day, it appears to use much more energy annually than it actually does.
The Delta T between the inside of the refrigerator and the ambient air affects efficiency: 2.25% to 2.5% per °F.
To calculate the correction factor, multiply the temperature difference by 2.5%.
If the kitchen is cooler than normal during metering, add the correction. If warmer, subtract. For example, if the kitchen is normally 72°F, but the temperature is 66°F during metering:
  1+ (2.5% x (72°F - 66°F)) = 1+ (0.025 x 6) = 1.15
Click to highlight the resulting correction factor: 1.15
Multiply the metered annual usage by 1.15 to get a more accurate picture of energy consumption, since the house is typically warmer than when metering occurred.

## Slide 39: Refrigerator Calculation
If existing refrigerator is metered, assuming typical ambient temperature during metering, kWh/year =
0.882 is a factor to adjust estimated energy usage since the crew asks the client not to open and close the refrigerator during metering.
Source: John Proctor
Metered usage (kWh)
Metering Duration (minutes)
x 60
minutes
hour
hours
year
x 8,760
0.882
Base Load Measures
GJA 2024 Version III
39
Notes: Here is the complete calculation converting meter reading to annual estimated usage. In this calculation, we assume that interior temperatures were typical during metering, so there is no temperature adjustment:
Walk through the calculation. Divide metered usage by the duration of metering, in minutes, and then multiply by 60 to get hourly usage. Multiply that by 8,760 hours a year to get annual usage. Divide this number by 0.882 since the crew asks client not to open the refrigerator during metering, but normally the refrigerator would be opened and closed occasionally, resulting in higher energy use.2
  2Correction factor thanks to John Proctor, PE, Proctor Engineering Group.

## Slide 40: Can’t Always Meter
Not always possible to meter the refrigerator.
  Cannot move fridge without damaging floor.
  Difficult access due to cabinets, furniture, stove, etc.
  Receptacle suspect.
When metering is not possible, use Association of Home Appliance Manufacturers (AHAM) database for energy use of existing refrigerators.
GJA 2024 Version III
40
Notes: It is not always possible to meter the refrigerator.
  Sometimes you can’t move the fridge without damaging the floor.
It may be difficult to access the fridge due to cabinets, furniture, stove, etc.
The receptacle is suspect, i.e., it won’t plug into the metering device or appears unsafe.
When metering is not possible, use the AHAM database for energy use of existing refrigerators.
If the refrigerator cannot be found in the database, use the chart from Appendix B of the Refrigerator Info Toolkit to translate model and serial numbers to date of manufacture. Generally speaking, if the refrigerator was made in 2003 or later, it will not qualify for replacement.

## Slide 41: Adjust for Age
Refrigerator Age | AHAM Energy Data is Inflated By:
Less than 5 years old | 0%
5 to 10 years old | 10%
10 to 15 years old | 20%
More than 15 years old | 30%
Refrigerator efficiency degrades between 1% and 2% per year of operation.
NEAT tool accounts for this in audit.
When using database instead of metering, correct for age of appliance.
NEAT Adjustments to AHAM Appliance Energy Data for Refrigerator Age
GJA 2024 Version III
41
Notes: When relying on the database, adjust for the decline in performance over time.
Refrigerator efficiency degrades between 1% and 2% per year of operation.
The approved computerized audit tools accounts for this in the audit.
When using the database instead of metering, correct for the age of the appliance.

## Slide 42: Control Settings Matter
Source: Larry Kinney, E Source, Boulder, CO, 2001
Energy Use of a 15 ft3 Maytag
GJA 2024 Version III
42
Notes: Chart: Energy use of a 15-cubic-foot Maytag refrigerator.3
Some refrigerators may not qualify for replacement in the WAP, but changing the settings can result in noticeable energy savings for the client.
In a hot climate with an ambient temperature of 90F, changing the fresh food compartment setting from 36.4F to 43.9F (-9.1F up to 12.4F for the freezer) will save the client over 200 kWh/year.
3 Larry Kinney, E Source, Boulder, CO, 2001.

## Slide 43: Other Refrigerators Issues
Replacement refrigerators must comply with UL 250.
Must properly dispose replaced units per Clean Air Act 1990, section 608, as amended by 40 CFR 82, 5/14/93.
Cost of disposal, if any, should be reflected in SIR calculation.
GJA 2024 Version III
43
Notes: Replacement refrigerators must comply with UL 250. This label reflects compliance with federal regulations.
Dispose of old units according to the Clean Air Act of 1990, section 608, as amended by 40 CFR 82, 5/14/93.
  The old unit may not remain at the client’s home or go to another home. The purpose of replacing inefficient refrigerators is to get them off the grid. Decommissioning is necessary to ensure that the WAP doesn’t inadvertently create a black market in second-hand refrigerators.
The cost of disposal, if any, should be reflected in the SIR calculation.

## Slide 44: Clean Refrigerator Coil
Even if replacement is not an option, some savings are possible.
 | Average | High
Energy Savings | 36 kWh/yr | 200 kWh/yr
$ Savings* | $3.96/yr | $22.00/yr
Frequency of coil cleaning | Once/year, 3% savings | Never been cleaned
* Savings based on $0.11/kWh
Base Load Measures
GJA 2024 Version III
44
Notes: Table of estimated energy savings from cleaning a refrigerator coil
Even if replacement is not an option, some savings are possible.
The refrigerator will function more efficiently if the coil is clean and has a few inches of air space around it (i.e., it’s not pushed right up to the wall).
If the coil has never been cleaned, doing so could save up to 200 kWh/yr!
  Clean coils with the long, flat attachment on a vacuum cleaner and/or a long brush, similar to a bottlebrush.
Turn the refrigerator off before cleaning the coils. If it is built-in, turn off the circuit at the breaker.

## Slide 45: Water Heating
Assess condition of appliance.
Test draft of gas water heaters. (more information in Combustion Appliances section)
Adjust set temperature.
Insulate tank and first 6 feet of pipes.
Replacement.
Reduce hot water use.
Base Load Measures
GJA 2024 Version III
45
Notes: Assess the condition of the appliance.
Test the draft of gas water heaters. (For more detail, refer to the Combustion Appliance section of this curriculum)
Adjust the set temperature and insulate the tank and the first 6 feet of pipes if the tank is in good working order.
Replace the unit if needed.

## Slide 46: Assess Condition
Damaged?
Rusty or corroded?
Leaking?
Photo courtesy of US Department of Energy
This unsheltered water heater is less than 6 months old.
GJA 2024 Version III
46
Notes: Assess the condition of the water heater to determine if a replacement might be necessary as a health and safety measure. Is the tank:
Damaged?
Rusty or corroded?
Leaking?

## Slide 47: Adjust Set Temperature
Mark original position of dial.
Verify water temperature.
Set back to 120°F.
Adjust as needed.
Photo courtesy of US Department of Energy
GJA 2024 Version III
47
Notes: Many clients have the temperature set as high as 140F, though 120F is adequate for most homes. The lower temperature saves energy and prevents scalding.
Mark the original position of the dial. The labeling around the dial can be off, so it’s important to mark a reference point before changing anything.
Verify the water temperature. Run water from the hot tap closest to the water heater to measure.
Set back to 120F.
Adjust as needed.

## Slide 48: Reduce Setting from 140°F to 120°F
 | Average | High
Energy Savings | 343 kWh/yr | 974 kWh/yr
$ Savings* | $37.73/yr | $107.14/yr
Existing DHW Use | 4,500 kWh/yr | 6,500 kWh/yr
* Savings based on $0.11/kWh
GJA 2024 Version III
48
Notes: If the existing hot water heater is using 4,500 kWh/yr, setting the temperature back from 140F to 120F can save 343 kWh/yr, or almost $40 at $0.11/kWh.

## Slide 49: Insulate
Don’t insulate too close to the flame on gas water heaters. 9”
Insulation too close to flame
GJA 2024 Version III
49
Notes: Specify that elbows should be insulated correctly, with insulating sleeves cut at a 45-degree angle to cover the joint.
On gas water heaters, pipe insulation can present a fire hazard if installed too close to the burner.

## Slide 50: Replacement
Replacement can be based on:
Audit.
Water Heater Guide on WAPTAC.
Health & Safety.
Can replace existing water heater in eligible households with:
Standard tank water heaters.
Whole Home Tankless.
Heat Pump Water Heaters.
Solar Water Heaters.
Images courtesy of www.energystar.gov
GJA 2024 Version III
50
Notes: Replacement can be based on:
Audit results.
Water Heater Info Toolkit on WAPTAC.
Health and safety concerns.
Replace an existing water heater in eligible households with:
Standard tank water heater.
Whole home tankless water heater.
Heat pump water heater.
Solar water heater.

## Slide 51: Hot Water Use
Cut down on hot water use by repairing leaks and installing low-flow fixtures.
Source: 2008 Buildings Energy Databook. US DOE
6% Faucet Flow
20% Bath Filling
Showers 37%
Clothes Washer 14%
Dishwasher 10%
14% Sink Filling
GJA 2024 Version III
51
Notes: Chart shows typical hot water use by end use in the home.
Cut down on hot water use by repairing leaks and installing low-flow fixtures.

## Slide 52: Repair Leaky Hot Water Tap
 | Average | High
Energy Savings | 144 kWh/yr | 3,000 kWh/yr
$ Savings* | $15.84/yr | $330/yr
Leakage | 2 drips/min | 1 drip/sec
* Savings based on $0.11/kWh
GJA 2024 Version III
52
Notes: Repairing a hot water tap leaking 2 drops/minute can save almost $16/yr based on $0.11/kWh.
Repairing larger leaks save substantially more. Repairing a hot water leak dripping at the rate of 1 drop/second will save over $300/year based on the same energy prices.

## Slide 53: Low-Flow Fixtures
Reduce Hot Water Consumption
Showers: Replace faucets with flow of ≥ 3 gpm.
Lavatory faucets: Install faucet aerators if none exist.
Kitchen faucets: Install faucet aerators if none exist.
GJA 2024 Version III
53
Notes: Reduce hot water consumption:
Showers: Replace showerheads that have a flow ≥ 3 gpm with low-flow showerheads.
Lavatory faucets: Install faucet aerators if none exist.
Kitchen faucets: Install faucet aerators if none exist.

## Slide 54: Other Base Load Intervention
Remove Dryer Vent Restriction
 | Average | High
Energy Savings | 227 kWh/yr | 455 kWh/yr
$ Savings* | $24.97/yr | $50.05/yr
% Savings on 364 Loads/Year | 25% | 50%
* Savings based on $0.11/kWh
GJA 2024 Version III
54
Notes: Remove dryer vent restrictions.
When dryers must force air through constricted spaces, they must work harder and it takes longer to dry a load of clothes.
Creating a smooth, open pathway for dryer exhaust can save up to $50/year through improved dryer performance.
Refer to the Dryer Vent section of the Installer Intermediate curriculum for more details on dryer exhaust protocols.

## Slide 55: Summary
Base load refers to all non-seasonal energy use within the home.
About half of home energy use is for base load requirements.
Utility bill assessment helps the auditor determine base load usage and related savings potential.
Typical measures include lighting retrofits, refrigerator replacement, hot water heater modification or replacement, and reduction of hot water use.
GJA 2024 Version III
55
Notes: Base load refers to all non-seasonal energy use within the home.
About half of home energy use is for base load requirements.
A utility bill assessment helps the auditor determine base load usage and the related savings potential.
Typical measures include lighting retrofits, refrigerator replacement, hot water heater modification or replacement, and reduction of hot water use.