## Slide 1: Math Basics
WEATHERIZATION ENERGY AUDITOR SINGLE FAMILY
GJA 2024 Version III
4

## Slide 2: Learning Objectives
By attending this session, participants will:
Working with units.
Working with areas and volumes.
Calculating ASHRAE requirements
Calculating CFM50 vs. ACH.
Estimating bags of cellulose.
Calculating appropriate attic and foundation venting.
Refrigerator usage calculations.
Lighting retrofit savings calculations.
Math basics
GJA 2024 Version III
2
Notes: By attending this session, participants will:
Working with units.
Working with areas and volumes.
Calculating building tightness limits.
Calculating CFM50 vs. ACH.
Estimating bags of cellulose.
Calculating appropriate attic and foundation venting.
Refrigerator usage calculations for determining replacement eligibility.
Lighting retrofit savings calculations.

## Slide 3: Typical Units
Surface Area
Length x Width (feet x feet)
Units are square feet (sq. ft., ft2)
Volume
Length x Width x Height
Units are cubic feet (cu. ft., ft3)
Air Flow
Volume per unit time
Units are cubic feet per minute (ft3/min, CFM)
Air changes per hour - Need to know house volume
GJA 2024 Version III
3
Notes: Surface area:
Length x width (feet x feet).
Units are square feet (sq. ft., ft2).
Volume:
Length x width x height.
Units are cubic feet (cu. ft., ft3).
Airflow:
Volume per unit of time.
Units are cubic feet per minute (ft3/min, CFM).
Air changes per hour  need to know house volume to calculate ACH.

## Slide 4: Floor Area
Use sketch of floor plan.
Note unconditioned area.
Calculate conditioned area.
Unconditioned
Conditioned
GJA 2024 Version III
4
Notes: Use sketch of floor plan.
Note unconditioned area.
Calculate conditioned area.

## Slide 5: Calculate Conditioned Area
Area = Length x Width.
Final units = Square Feet.
Tackle floor plans in pieces.
Reduce complicated shapes into small, simple shapes.
GJA 2024 Version III
5
Notes: Area = length x width.
Final units = square feet.
Tackle floor plans in pieces.
Reduce complicated shapes into small, simple shapes.
Calculating area is useful for insulation estimating.
Floor area is used later to calculate the conditioned volume, which is used to determine ACH, MVR, and cost-effectiveness of certain heating and cooling measures.

## Slide 6: Calculate Conditioned Area
180 ft2
128 ft2
416 ft2
+ 416 ft2
1,140 ft2
12’ x 15’ =
16’ x 26’ =
16’ x 8’ =
Main House
1 ½ Stories
Double area
180 ft2
128 ft2
416 ft2
GJA 2024 Version III
6
Notes: Give the students calculators, pencils, and scrap paper of the “Conditioned Area Worksheet” and let them calculate the answers before going on.
Click to reveal areas of various sections of the home and the total.

## Slide 7: Volume – Keep the Units Straight
Keep the units straight:
= ft2
Square Feet x Feet = Cubic Feet
ft2 x ft = ft3
Cubic Feet ÷ Feet = Square Feet
= ft2
ft
ft3
GJA 2024 Version III
7
Notes: Keep the units straight:
Square feet x feet = cubic feet
Ft2 x ft = ft3
Cubic feet ÷ feet = square feet
Ft3/ft = ft2

## Slide 8: Calculate Conditioned Volume
Ell = 180 ft2 x 7’6” = ___
Rear Addition = 128 ft2 x 7’ 5” = ___
Main House, 1st Fl = 416 ft2 x 8 = ___
Main House, 2nd Fl = Attic Flat = 8’
Eaves Wall = 3’
GJA 2024 Version III
8
Notes: Areas listed as previously calculated.
Ceiling heights noted from walk-through.
Let students jot down numbers or perform calculations with the slide up. Answers will be revealed two slides later.
Q. Why don’t we include attic spaces in these volume calculations?
A. Those spaces are unconditioned, so the volumes aren’t useful for calculating MVR or ACH. We only need to know the volume of air that is part of the living space and that the client pays to heat or cool.

## Slide 9: Keep the Units Straight
1 ft x 1 ft = 1 ft2
12 in x 12 in = 144 in2 = 1 ft2
300 in x 200 in = 60,000 in2
60,000 in2
144 in2/ft2
= 417 ft2
GJA 2024 Version III
9
Notes: Calculating feet and inches can get tricky. Each foot is 12 inches long, so a square foot contains 12 x 12 square inches:
1 ft x 1 ft = 1 ft2
12 in x 12 in = 144 in2 = 1 ft2
300 in x 200 in = 60,000 in2
60,000 in2  144 in2/1 ft2 = 417 ft2

## Slide 10: Calculate Conditioned Volume
Ell = 180 ft2 x 7’6” = 1,350 ft3
Rear Addition = 128 ft2 x 7’ 5” = 950 ft3
Main House, 1st Fl = 416 ft2 x 8 = 3,328 ft3
Main House, 2nd Fl = Attic Flat = 8’
Eaves Wall = 3’
Ceiling Height = 7’
GJA 2024 Version III
10
Notes: The lower floor of the home, including the addition and ell, are simple rectangles and easy to calculate.
Ell = 180 ft2 x 7’6” = 1,350 ft3
Rear addition = 128 ft2 x 7’5” = 950 ft3
Main house, first floor = 416 ft2 x 8’ = 3,328 ft3
The second floor of the main house (the only section with a second story) is an odd shape due to the sloping ceiling and knee-wall attics. With the following information, we can accurately calculate the volume:
Main house, second floor:
Attic flat = 8’
Eaves wall = 3’
Ceiling height = 7’

## Slide 11: Odd Shapes
Area:
Triangle = ½ Base x Height
Circle = πr2 ; π ≈ 3.14
Volume: (Area x 3rd Dimension)
Triangle = ½ Base x Height x Length
Cylinder = πr2 x Height
GJA 2024 Version III
11
Notes: Break complex shapes down into simple components, circles, triangles, and rectangles, and use these formulas:
Area
  Triangle = ½ base x height
Circle = πr2 ; π ≈ 3.14
Volume = area * 3rd dimension
  Triangle = ½ base x height x length
Cylinder = πr2 x height

## Slide 12: Conditioned Volume: 2nd Floor
Tackle Complex Shapes.
Break down into simple shapes.
Second Story
Main House, 2nd Fl = Attic Flat = 8’
Eaves Wall = 3’
Ceiling Height = 7’
GJA 2024 Version III
12
Notes: Break down into simple shapes.
This can be broken down in a number of ways. For our example, we will break it down into two rectangles and two triangles.
Dimensions from walk-through:
Attic flat = 8’
Eaves wall = 3’
Ceiling height = 7’

## Slide 13: Calculating Volume: 2nd Floor
832 ft3
1,248 ft3
+ 416 ft3
2,496 ft3
2nd Floor Volume:
Top Rectangle = 8 ft x 4 ft x 26 ft = 832 ft3
* Volume of a triangle = ½ Base x Height x Length
2 Triangles* = 2 x (½ (4 ft x 4 ft) x 26 ft) = 416 ft3
Bottom Rectangle = 16 ft x 3 ft x 26 ft = 1,248 ft3
GJA 2024 Version III
13
Notes: Let students calculate the various shapes’ volumes and then the total.
Click to reveal answers on the slide.
Top rectangle = 8’ x 4’ x 26’ = 832 ft3
Bottom rectangle = 16’ x 3’ x 26’ = 1,248 ft3
2 triangles = 2 x (½ (4’ x 4’) x 26’) = 416 ft3
Total conditioned volume of 2nd floor = 2,496 ft3

## Slide 14: Calculate Conditioned Volume
Ell = 1,350 ft3
Rear Addition = 950 ft3
Main House, First floor = 3,328 ft3
Main House, Second floor = 2,496 ft3
TOTAL = 8,124 ft3
But the total floor area x 8 can get you close:
1,140 ft2 x 8 ft = 9,120 ft3
GJA 2024 Version III
14
Notes: The final step is to add up the volumes of all the sections of the house:
Ell = 1,350 ft3
Rear addition = 950 ft3
Main house, first floor = 3,328 ft3
Main house, second floor = 2,496 ft3
Total = 8,124 ft3
But the total floor area x 8’ can get you close:
1,140 ft2 x 8’ = 9,120 ft3

## Slide 15: Indoor Air Quality “At Risk” Calculation
At Risk Calc:
For Example:
• 8,400 ft3 minimum
• 2,100 ft3 for each occupant beyond 4
• Compare to actual heated volume
• 5 occupants: 5 - 4 = 1
• 1 x 2,100 ft3 = 2,100 ft3
• 8,400 ft3 + 2,100 ft3 = 10,500 ft3
Our sample home with a volume of 8,124 ft3 is less than the 10,500 ft3 minimum, and is considered “At Risk”.
GJA 2024 Version III
15
Notes: When blower door testing is not possible, some states require the auditor to determine if the home is “at risk” for moisture and IAQ problems. Blower door results supersede this calculation.
At risk calculation:
8,400 ft3 minimum.
2,100 ft3 for each person over 4 occupants.
Compare to actual heated volume.
  5 occupants in our sample home: 5 – 4 = 1
1 x 2,100 ft3 = 2,100 ft3 additional space needed to avoid being “at risk”
8,400 ft3 + 2,100 ft3 = 10,500 ft3
Sample home: 8,124 ft3
Click to reveal that sample home is “at risk.”
  Home volume of 8,124 ft3 is less than the 10,500 ft3 minimum and is considered “at risk.” With no way to test the actual ACH of the home, most programs would not air seal a home with “at risk” status.

## Slide 16: Dividing by Fractions
Dividing by a fraction is the same as multiplying by the reciprocal.
Reciprocal of ½ is , or 2.
10 ÷ ½ = 10 x = 10 x 2 =
= 10 x = 10 x 2 =
= x = = = 1½ =
2
1
2
1
½
10
½
3
4
3
4
2
1
6
4
3
2
2
1
20
20
1.5
GJA 2024 Version III
16
Notes: Dividing by a fraction is the same as multiplying by the reciprocal.
Reciprocal of ½ is 2/1, or 2.
Click to reveal answers to the calculations.
Distribute “Dividing by Fractions Worksheet.” Let students complete and then provide answers.

## Slide 17: Air Changes per Hour
Volume of conditioned space = 8,124 ft3
Blower door reading = 2,000 CFM50
ACH50 = 2,000 CFM50 x 60 / 8,124 ft3
=
ACH50 = CFM50 x 60min/hr ÷ Volume
14.77 Air Changes per Hour at 50 Pa
GJA 2024 Version III
17
Notes: To calculate air changes per hour, convert the blower door reading (taken in cubic feet per minute at 50 Pascals) to hours by multiplying by 60 (number of minutes per hour), then dividing by the volume:
ACH50 = CFM50 x 60 min/hr ÷ volume
Volume of conditioned space: 8,124 ft3
Blower door reading = 2,000 CFM50
Click to reveal answer.
ACH50 = 2,000 CFM50 x 60 ÷ 8,124 ft3 = 14.77 ACH at 50 Pa

## Slide 18: Percent Infiltration Reduction
% Reduction Goal
If ACH50 = 11-17, goal is 25%.
If ACH50 = 18-22, goal is 35%.
If ACH50 > 23, goal is 40%.
Example
ACH50 = 14.77, goal is 25%.
100% - 25% = 75% of Pre-Weatherization CFM50 is goal.
Pre-Weatherization 2,000 CFM50
2,000 CFM50 x 75% = 2,000 x 0.75 = 1,500 CFM50
GJA 2024 Version III
18
Notes: Some programs use percent infiltration reduction tables to guide air sealing. Calculating the percent infiltration reduction provides us with the blower door target.
Sample % reduction goals:
  If ACH50 = 11-17, goal is 25%
If ACH50 = 18-22, goal is 35%
If ACH50 > 23, goal is 40%
Example:
  ACH50 = 14.77, goal is 25% infiltration reduction
100% - 25% = 75% of pre-weatherization CFM50 is the goal
To determine air-sealing goal, target CFM50:
  Pre-weatherization 2,000 CFM50
  2,000 CFM50 x 75% = 2,000 x 0.75 = 1,500 CFM50

## Slide 19: Estimating Attic Insulation
Attic Area = Main House + Addition + Ell =
Main House Attic = 8’ * 26’ = 208 ft2
Addition = 128 ft2
Ell = 180 ft2
Total Attic Area = 516 ft2
Bring Attic from R-0 to R-40
GJA 2024 Version III
19
Notes: We will use our sample house from before to estimate attic insulation:
Attic area = main house + addition + ell =
  Main house attic = 8’ x 26’ = 208 ft2
Addition = 128 ft2
Ell = 180 ft2
Total attic area = 516 ft2
Bring attic from R-0 to R-40.

## Slide 20: Estimating Attic Insulation
Sample Coverage Chart for Blown-In Cellulose |  |  |  |  |  |  | 
R-Value @ 75° Mean Temp. | Minimum Thickness (inches) |  | Maximum Net Coverage (No adjustment for framing) |  |  | Gross Coverage (based on 2” x 6” framing on 16” centers) | 
To obtain a thermal resistance of: | Installed insulation shouldn’t be less than: | Thickness after settling | Max. Sq. Ft. per Bag | Min. Bags per 1,000 Sq. Ft. | Min. Weight per Sq. Ft. (lbs) | Max. Sq. Ft. per Bag | Min. Bags per 1,000 Sq. Ft.
R-50 | 15.0 | 13.5 | 13.8 | 72.7 | 1.689 | 14.3 | 69.9
R-42 | 12.6 | 11.4 | 16.4 | 61.0 | 1.419 | 17.2 | 58.3
R-40 | 12.0 | 10.8 | 17.2 | 58.1 | 1.351 | 18.1 | 55.4
R-38 | 11.4 | 10.3 | 18.1 | 55.2 | 1.284 | 19.1 | 52.4
R-32 | 9.6 | 8.6 | 21.5 | 46.5 | 1.081 | 22.9 | 43.7
R-30 | 9.0 | 8.1 | 22.9 | 43.6 | 1.014 | 24.5 | 40.8
R-25 | 7.5 | 6.8 | 27.5 | 36.3 | 0.845 | 39.8 | 33.6
R-24 | 7.2 | 6.5 | 28.7 | 34.9 | 0.811 | 31.2 | 32.1
R-22 | 6.6 | 5.9 | 31.3 | 32.0 | 0.743 | 34.3 | 29.2
R-19 | 5.7 | 5.1 | 36.2 | 27.6 | 0.642 | 40.0 | 25.0
R-13 | 3.9 | 3.5 | 52.9 | 18.9 | 0.439 | 58.4 | 17.1
R-11 | 3.3 | 3.0 | 62.6 | 16.0 | 0.372 | 69 | 14.5
GJA 2024 Version III
20
Notes: The sample coverage chart, usually part of the insulation packaging, is used to determine how much insulation will be needed for the attic.
This chart shows how thick the insulation should be to reach R-40 (12 inches).
Click to circle appropriate installed thickness.
The chart includes how many square feet of coverage each bag will provide at that installed depth.
Click to reveal arrow pointing to gross coverage per bag for desired R-value.

## Slide 21: Estimating Attic Insulation #1
Total Attic Area = 516 ft2
Bring Attic from R-0 to R-40
At R-40 w/ 2x6, 16” oc., 1 bag covers 18.1 ft2*
Assume 15% waste allowance.
How many bags do you need for the attic?
* From sample coverage chart
GJA 2024 Version III
21
Notes: Total attic area = 516 ft2
Bring attic from R-0 to R-40
At R-40 with 2 x 6 studs, 16” o.c., 1 bag covers 18.1 ft2*
Some installers use a general rule of thumb to account for spillage or over-packing: Assume 15% waste allowance.
* From sample coverage chart.
How many bags do you need for the attic?
Let students calculate the answer before proceeding to the next slide.

## Slide 22: Estimating Attic Insulation #2
Total Attic Area = 516 ft2
Bring Attic from R-0 to R-40
Assume 15% waste allowance
516 ft2 ÷ 1 bag/18.1 ft2 = 28.5 bags of insulation
28.5 x 1.15 = 32.78 bags = 33 bags (always round up)
GJA 2024 Version III
22
Notes: Total attic area = 516 ft2
Bring attic from R-0 to R-40
516 ft2 ÷ 1 bag/18.1 ft2= 28.5 bags of insulation
Click to reveal units cancelling each other out.
Assume 15% waste allowance.
Click to reveal number of bags.
28.5 x 1.15 = 32.78 bags = 33 bags (always round up)

## Slide 23: Keep the Units Straight
3.5 lbs/ft3 x 1,000 ft3 = 3.5
lbs
ft3
x 1,000 ft3 = 3,500 lbs
3,500 lbs
36 lbs/bag
= 3,500 lbs x
bag
36 lbs
= 97.2 bags
Label units to keep track.
Units on top and bottom cancel each other out.
Have seen “Gallons of electricity”!!!
GJA 2024 Version III
23
Notes: Label units to keep track.
Units on top and bottom cancel each other out.
Have seen “Gallons of electricity” on some spreadsheets where the data collector mixed up units.
Click to reveal units cancelling each other out.

## Slide 24: Estimating Wall Insulation
How many bags to dense-pack 1,200 ft2 of wall with 2 x 4 studs, 16” o.c.?
Sample Wall Coverage Chart
Maximum Coverage |  |  |  | 
Sidewalls | Thickness (inches) | Square Feet per Bag |  | Weight per Square Foot
 |  | 16” O.C. | 24” O.C. | 
R-13 (2x4) | 3.5 | 33.8 | 32.7 | 0.758
R-20 (2x6 | 5.5 | 21.5 | 20.8 | 1.192
1,200 ft2 = 35.5 bags = 36 bags
33.8 ft2/bag
GJA 2024 Version III
24
Notes: Sample Coverage Chart
How many bags do we need to dense pack 1,200 ft2 of wall with 2 x 4 studs, 16”o.c.?
1,200 ft2/33.8 ft2/bag = 35.5 bags = 36 bags
Always assume 15% waste allowance. (Total with waste allowance is 35.5 x 1.15 = 41 bags)

## Slide 25: Estimating Wall Insulation
Each sq ft of wall contains: 1 ft x 1 ft x 3.5 inches = 0.2917 ft3
12 in/ft
0.758 lbs/ft2 = 2.6 lbs/ft3
0.2917 ft3/ft2
What density does the chart assume?
Maximum Coverage |  |  |  | 
Sidewalls | Thickness (inches) | Square Feet per Bag |  | Weight per Square Foot
 |  | 16” O.C. | 24” O.C. | 
R-13 (2x4) | 3.5 | 33.8 | 32.7 | 0.758
R-20 (2x6 | 5.5 | 21.5 | 20.8 | 1.192
Chart indicates 0.758 lbs/sq ft
What? So low?
Not really, that accounts for space taken up by framing
GJA 2024 Version III
25
Notes: What density does the chart assume?
Click to cancel out units and circle the answer.
If we calculate the actual volume based on square feet and then use the weight per square foot data from the table, it appears following the chart would result in an installed density of only 2.6 lbs/ft3.
Click to bring text box into view.
The installed density isn’t really as low as it appears in these calculations. The difference is made up with framing within the walls. They reduce the actual volume being insulated.

## Slide 26: Estimating Wall Insulation
Assume 3.5 lbs/ft3 & 36 lbs/bag.
1,200 ft2 x 3.5 inches = 350 ft3
12 in/ft
350 ft3 x 3.5 lbs/ ft3 = 1,225 lbs
1,225 lbs = 34.03 bags = 35 bags
36 lbs/bag
What if there’s no coverage chart? The math is simple:
How many bags to dense-pack 1,200 ft2 of wall with 2 x 4 studs, 16” o.c.?
Same as the chart
GJA 2024 Version III
26
Notes: What if there is no coverage chart? The math is simple:
How many bags to dense pack 1,200 sq. ft. of wall with 2 x 4 studs, 16”o.c.?
Click to reveal math.
Assume 3.5 lbs/ft3 and 36 lbs/bag.
1,200 ft2 x 3.5 inches = 350 ft3
12 in/ft
350 ft3 x 3.5 lbs/ ft3 = 1,225 lbs
1,225 lbs = 34.03 bags = 35 bags
36 lbs/bag
We get essentially the same result as when using the information from the coverage chart.

## Slide 27: Calculate Wall Insulation: Sample House
Calculate total wall area.
Subtract windows and doors.
Conditioned
Unconditioned
GJA 2024 Version III
27
Notes: To estimate the amount of insulation for dense packing the sidewalls:
Calculate total wall area.
Subtract windows and doors.

## Slide 28: Estimate Wall Insulation: Sample House
Main House
First Floor = 2(16’ x 8’) + 2(26’ x 8’) =
2nd Floor = 2(3’x 26’) + 2(6’ x 26’)* + 2(16’ x 7’) =
Addition = 2(8’ x 7’5”) + (16’ x 7’5”)** =
Ell = (12’ x 7’6”)***+ 2(15’ x 7’6”) =
* Sloped ceiling, from walk-through notes
** Only count one long wall, other wall abuts the home
*** Only count one short wall, other wall abuts the home
672 ft2
692 ft2
237 ft2
315 ft2
GJA 2024 Version III
28
Notes: Calculate total wall area:
Main house, first floor = 2 (16’ x 8’) + 2 (26’ x 8’) =
Main house, 2nd floor = 2 (3’ x 26’) + 2 (6’ x 26’)* + 2 (16’ x 7’) =
Addition = 2 (8’ x 7’5”) + (16’ x 7’5”)** =
Ell = (12’ x 7’6”)***+ 2(15’ x 7’6”) =
*Sloped ceiling, from walk-through notes
** Only count one long wall; other wall abuts the home.
*** Only count one short wall; other wall abuts the home.
Let students perform calculations, then click to reveal the answers.
Main house, first floor = 2 (16’ x 8’) + 2 (26’ x 8’) = 672 ft2
Main house, 2nd floor = 2 (3’ x 26’) + 2 (6’ x 26’)* + 2 (16’ x 7’) = 692 ft2
Addition = 2 (8’ x 7’5”) + (16’ x 7’5”)** = 237 ft2
Ell = (12’ x 7’6”)***+ 2 (15’ x 7’6”) = 315 ft2

## Slide 29: Wall Insulation: Sample House
Add total wall area
Subtract doors and windows
  Heated space windows & doors:
      8 Windows, 12.5 ft2 each 8 x 12.5 ft2 = 100 ft2
      2 Doors, 20 ft2 each 2 x 20 ft2 = 40 ft2
    Window & Door Area = 140 ft2
Wall Area Needing Insulation =
      +
672 ft2
692 ft2
237 ft2
+ 315 ft2
1,916 ft2
- 140 ft2
1,776 ft2
GJA 2024 Version III
29
Notes: Add total wall area.
Subtract doors and windows.
Heated space windows and doors:
8 windows, 12.5 ft2 each
8 x 12.5 ft2 = 100 ft2
2 doors, 20 ft2 each
2 x 20 ft2 = 40 ft2
Window & door area = 140 ft2
Let students perform the calculations.
Click three times to reveal calculated total wall area, windows and doors area, and the resulting wall area needing insulation.

## Slide 30: Estimating Wall Insulation: Sample House
How many bags to dense-pack 1,776 ft2 of wall with 2 x 4 studs, 16” o.c.?
Sample Wall Coverage Chart
Maximum Coverage |  |  |  | 
Sidewalls | Thickness (inches) | Square Feet per Bag |  | Weight per Square Foot
 |  | 16” O.C. | 24” O.C. | 
R-13 (2x4) | 3.5 | 33.8 | 32.7 | 0.758
R-20 (2x6 | 5.5 | 21.5 | 20.8 | 1.192
1,776 ft2 = 52.5 bags = 53 bags
33.8 ft2/bag
GJA 2024 Version III
30
Notes: Now we have the total wall area needing insulation. How many bags of insulation will be needed?
Click to reveal arrow on sample coverage chart pointing at square feet of coverage per bag.
Dividing the wall area by the estimated square feet of coverage per bag gives us the number of bags needed for the job.
Click to reveal calculation and answer.

## Slide 31: Attic Venting
1 ft2 NFA of vent needed for every 300 ft2 of attic*.
If vents are located high and low to induce ventilation, 1 ft2 of vent needed for every 600 ft2 of attic.
1,000 ft2 attic with gable vents.
  1,000 ft2 / 600 ft2 = 1.67 ft2 of vent needed.
  Two existing gable vents each 12”x10”.
  2 x 12” x 10”/144 = 1.67 ft2 of existing vent.
Is existing venting adequate?
* Assumes ceiling vapor barrier.
No, must use NFA.
GJA 2024 Version III
31
Notes: 1 ft2 NFA of vent needed for every 300 ft2 of attic*
1,000 ft2 attic with gable vents
1,000 ft2/600 ft2 = 1.67 ft2 of vent needed
Two existing gable vents each 12” x 10”
2 x 12” x 10”/144=1.67 ft2 of existing vent
Is existing venting adequate?
* Assumes a vapor barrier (painted ceiling).
Click to reveal the answer: No. Total vent area is not the same as NFA.
Refer to Attic Ventilation section of this curriculum for more details.

## Slide 32: Foundation Venting
1 ft2 of vent needed for every 1,500 ft2 of crawl space.
1,000 ft2 crawl space.
1,000 ft2 =
1,500 ft2
0.67 ft2 of vent needed
96 in2 NFA
0.67 ft2 x 144 in2/ft2 =
GJA 2024 Version III
32
Notes: If foundation venting is required, these are usually the guidelines:
1 ft2 of vent NFA needed for every 1,500 ft2 of crawl space with a ground vapor retarder.
Perform sample calculation based on a 1,000 ft2 crawl space:
Let students calculate, then click to reveal the answers.
1,000 ft2/1,500 ft2 = 0.67 ft2 of vent needed
0.67 ft2 x 144 in2/ft2 = 96 in2 NFA

## Slide 33: Refrigerator Calculation
If existing refrigerator is metered, kWh/year =
0.882 is a factor to adjust estimated energy usage since the crew asks the client not to open and close the refrigerator during metering (Source: John Proctor).
Does not include 7% for defrost cycle.
Metered usage (kWh)
Metering Duration (minutes)
x 60
minutes
hour
hours
year
x 8760
0.882
GJA 2024 Version III
33
Notes: The metered usage of refrigerators is converted into kWh per year to determine if replacement is cost-effective.
0.882 is a factor to adjust estimated energy usage since the crew asks the client not to open and close the refrigerator during metering 1
Does not include 7% for defrost cycle
For more details on refrigerator metering, usage, and replacement, refer to the “Baseload Measures” section of this curriculum.
  1John Proctor et al. ôRefrigerator Metering: Parts 1 and 2, a Customer Energy Efficiency Program and Measurement and Evaluation Program.ö Prepared for Pacific Gas and Electric Company, September, 1994.

## Slide 34: Lighting Calculation
To calculate the energy saved through lighting retrofits we need:
Number of bulbs being replaced.
Wattage of existing bulbs.
Wattage of replacement bulbs.
Usage (hrs/day).
x
kW
1,000 Watts
Watts
fixture
4 ft x (60-13)
hours
day
days
year
x 6
x 365
= 412 kWh/yr
GJA 2024 Version III
34
Notes: By calculating the amount of watts saved when CFLs replace incandescent bulbs, we can estimate the energy savings of a CFL retrofit.
Need:
Number of replacements.
Wattage of existing bulbs.
Wattage of replacement bulbs.
Usage (hrs/day).
Calculation:
Replacing 4-60W incandescent bulbs that are on about 6 hours per day with 13W CFLs results in annual savings of 412 kWh/yr!
How much money would that save? Have students calculate based on local electricity rates. (Example: if local rates are $0.11/kWh annual savings equal 412 x 0.11 = $45.32)
For more details on lighting retrofits, refer to the “Base load Measures” section of this curriculum.

## Slide 35: Summary
Label units to keep them straight.
Area (square feet) = length x width.
Volume (cubic feet) = length x width x height.
All area, volume, ACH, and estimating calculations rely on basic functions: addition, subtraction, multiplication, and division.
Estimating bags of cellulose requires knowledge of framing type (for walls), and attic area and recommended R-values (for attics).
Attic and foundation venting calculations need NFA of vents, not just vent dimensions.
Refrigerator calculations in kWh/year determine cost-effectiveness of replacements.
Lighting savings calculations are based on wattage differences.
GJA 2024 Version III
35
Notes: Label units to keep them straight.
Area (square feet) = length x width.
Volume (cubic feet) = length x width x height.
All area, volume, BTL, ACH, and estimating calculations rely on basic functions: addition, subtraction, multiplication, and division.
Estimating bags of cellulose requires knowledge of framing type (for walls), and attic area and recommended R-values (for attics).
Attic and foundation venting calculations need NFA of vents, not just vent dimensions.
Refrigerator calculations in kWh/year determine cost-effectiveness of replacements.
Lighting savings calculations are based on wattage differences.