## Slide 1: General Construction and Carpentry
WEATHERIZATION ASSISTANCE PROGRAM STANDARDIZED CURRICULUM – December 2012
WEATHERIZATION ENERGY AUDITOR SINGLE FAMILY
GJA 2024 Version III
1

## Slide 2: Learning Objectives
By attending this session, participants will be able to:
Define residential house construction terminology.
Identify framing components.
Identify foundation, wall, roof, window, and door systems.
Recognize balloon and platform framing.
Understand how framing affects air leakage.
Understand installation of windows and doors.
GENERAL CONSTRUCTION AND CARPENTRY
GJA 2024 Version III
2
Notes: By attending this session, participants will be able to:
Define residential house construction terminology.
Recognize different structural framing types.
Identify different foundation, wall, roof, window, and door systems.
Recognize characteristics of balloon and platform framing.
Explain the impact that different framing types have on air leakage.
Review window and door installation processes.

## Slide 3
Photo courtesy of U.S. Department of Energy
GJA 2024 Version III
3
Notes: Take a look at this cross section of a typical house and point out the basic features such as the foundation, and the kinds of equipment that reside there. Move up to the living space and attic. Then point out some classic air leakage sites as labeled. Have students note the direction of air leakage.
The structure of a house, its framing, and other architectural features determine how a house loses heat. An understanding of how houses are put together and residential nomenclature are important to the auditor’s ability to communicate retrofit strategies to crews and contractors.

## Slide 4: House Framing Terminology
Illustration courtesy of Construction Invio.com
GJA 2024 Version III
4
Notes: This is an illustration of generalized construction of a residential structure.
Point out the parts on the slide and use the lab prop to test students on proper identification of the parts.
If helpful, create a slide that hides the labels and have students name the framing and other details as you point to them.

## Slide 5: Foundation Types
Slab on Grade Foundation
Basement or Crawl Space Foundation
Pier and Beam Foundation
Photo courtesy of PA WTC
Photo courtesy of Wikipedia
GJA 2024 Version III
5
Notes: Foundation characterisics of a basement include:
Basements are defined as full-height, below-grade structures that provide support for the home.
They contain the mechanical systems and often serve as limited use areas but may also be finished, full-use areas.
Temperature-moderating effects of the surrounding earth help maintain the interior space at a fairly constant temperature throughout the year.
Foundation characteristics of crawl spaces include:
Crawl spaces are constructed in the same manner as full basements but are more shallow.
Foundation heights up to three feet are typical.
They contain duct runs, plumbing, etc.
Because they are mostly above grade, unheated, and generally vented to the outside, the interior space experiences outside temperatures throughout the year.

## Slide 6: Visual Assessment - Perimeter
Box Sills are comprised of floor joists, rim joists, and mud sills.
Sit on the foundation.
Leaky: need to be air sealed.
Photo courtesy of U.S. Department of Energy
Rim Joist
Mud Sill
Floor Joists
GJA 2024 Version III
6
Notes: This is a photo of a box sill. The box sill shown is made up of the band joist and mud sill framing.
The box sill is a common perimeter leakage site in basements.

## Slide 7: Balloon Framing: 1840s to 1940s
Photo courtesy of the US Department of Energy
Illustration courtesy of Don Vandervort’s Home Tips.com
GJA 2024 Version III
7
Notes: Balloon framing is a style of framing that uses long, vertical framing for the exterior walls and some interior walls. These long "studs" extend uninterrupted from the sill on top of the foundation up to the roof eaves. Floor joists are fastened to, and supported by, ledger boards that extend around the interior perimeter of the exterior wall. Balloon framing was the most common type of wood-frame construction from the late 19th century through the late 1930s and is found throughout the entire United States.
The disadvantage of balloon framing from an energy standpoint are the numerous air pathways through the framed wall and floor cavities. Air coming in at the bottom of the house is warmed and rises to the attic.
Q: In addition to the leaky outside walls, can you name some other types of indirect air leakage commonly associated with balloon framed homes?
A: Plumbing chaseways, chimney chaseways, pocket doors, built in hutches, dropped ceilings in closets.

## Slide 8
Wall cavities and porch may be connected.
Air Leakage in Balloon Frame
Photo courtesy of the US Department of Energy
GJA 2024 Version III
8
Notes: This is a photo of a two-story house with balloon framing where the porch framing could be open to the wall cavities of the house.
This could be one of the largest hidden air leaks in the house, making it a good candidate for air sealing with dense-packed insulation.

## Slide 9: Platform Framing
Illustration courtesy of Don Vandervort’s Home Tips.com
Photo courtesy of the US Department of Energy
Cantilever
GJA 2024 Version III
9
Notes: Platform framing replaced balloon framing following in the late 1930s and is the most commonly used framing method today.
With platform framing, the exterior wall framing is fastened to a platform or deck made up of floor joists, a band joist, and subflooring. Subsequent stories are added by constructing additional platforms that are supported by the exterior wall below it. After the last set of walls are constructed, roof rafters or trusses are installed on the double top plate of the exterior walls.
Platform framing eliminates the need for draft stops that are required in balloon-framed walls, making this type of housing less susceptible to vertical air leakage than balloon framed walls.
Platform-frame houses still have their share of inherent air leakage problems.
Q: In the photo, note how the second level of this “split level” home cantilevers over the first level. What’s a potential problem there?
A: There may be holes or tears in the covering on the underside of the cantilevered floor, allowing outside air to enter the floor cavity between the two levels.

## Slide 10: Wall Construction Details
Illustration courtesy of Don Vandervort’s Home Tips.com
GENERAL CONSTRUCTION AND CARPENTRY
Drainage Plane
GJA 2024 Version III
10
Notes: Note the various components of a typical framed wall section including insulation, sheathing, house wrap, sheathing, and siding.
  Q: Is this an example of balloon framing or platform framing?
  A: Platform framing.
  Q: Why?
  A: It’s platform framing because it has a top plate, which is the horizontal framing member on the top of the vertical wall studs. Balloon framing does not use a top plate between first and second stories (see slide 6 and 8).

## Slide 11: Air Leakage in Platform Frame
Kitchen cabinets mounted under soffit or valance.
Graphic courtesy of Anthony Cox
GJA 2024 Version III
11
Notes: Pressure and thermal boundaries often become misaligned at dropped soffits.
This drawing shows a change in ceiling height and a dropped soffit, two causes for the gaps.
Even without a change in ceiling height, dropped soffits cause misalignment in the pressure and thermal boundaries. The pressure boundary, which is the sheetrock, drops below the level of the attic floor and is not typically sealed at the top.

## Slide 12: Air Leakage in Platform Frame
Inspect when in the attic.
Graphic courtesy of Anthony Cox
GJA 2024 Version III
12
Notes: If you see soffit-mounted cabinets in the kitchen, bathroom, or elsewhere, remember to investigate them when you inspect the attic.

## Slide 13: Changes in Ceiling Height
Graphic courtesy of Anthony Cox
GJA 2024 Version III
13
Notes: Often there is no wall cap in this kind of construction.
The open wall top allows even more heat loss, since the interior wall acts as a chimney, carrying conditioned air and moisture away from the conditioned space.

## Slide 14: Dropped Ceiling Over Closet
In older homes, gaps in pressure and thermal boundaries.
Photo courtesy of the US Department of Energy
GJA 2024 Version III
14
Notes: In older homes, the ceiling level changes in closets, causing gaps in the pressure and thermal boundaries.
The uninsulated bedroom and bathroom walls are exposed to essentially outdoor temperatures.
  Q: What kind of framing is this and why?
  A: Balloon framing because there’s no top plate on the closet ceiling.

## Slide 15: Knee Wall Attics
Graphic courtesy of Anthony Cox
GJA 2024 Version III
15
Notes: Knee wall attics, typical in 1½-story Cape Cod-style homes, are common sources of gaps in the pressure and thermal boundaries.
Even when the ceiling height of the living space below doesn’t change, the knee wall itself is usually uninsulated.
The interior wall is also often left without a top plate. Convective heat loss occurs through the wall cavity.

## Slide 16: Roof Construction Types
Illustration courtesy of finalarchitecture.com
Skillion and Lean-to Roof
Open Gable Roof
Box Gable Roof
Hip and Valley Roof
Gambrel Roof
Mansard Roof
Dutch Gable Roof
Hexagonal Gazebo Roof
Jerkinhead Roof
GJA 2024 Version III
16
Notes: These are illustrations of various roof types.
  Q: Of the many types of roof structures shown, pick the two most common residential roof types.
  A: 1) Gable roof and 2) hip and valley roof

## Slide 17: Roof Framing Details
Illustration courtesy of Don Vandervort’s Home Tips.com
GJA 2024 Version III
17
Notes:   Have students name the parts of the roof framing on the slide.
Note how the ridge beam double top plates tie in all of the common and valley rafters.

## Slide 18: Roof Features and Terms
Illustration courtesy of Jay Carter Roofing
GJA 2024 Version III
18
Notes: Note the exterior features of the roof.
Point out the exterior features of a roof.

## Slide 19: Roof Eaves Detail
Illustration courtesy of Cedar Shake and Shingle Bureau
GJA 2024 Version III
19
Notes: Note detail of the roof eave and how the insulation blanket is a consistent depth all of the way out to the exterior wall. Also illustrated is the flow of passive ventilating air from the eaves through the ridge and gable vent.

## Slide 20: Window Terminology
Trim
Glass Plane
Head Jamb
Upper Sash
Side Jamb
Lower Sash
Stop
Sill (sloped)
Typical Wood Window
Exterior
Image developed for US DOE WAP National Standardized Curricula
GJA 2024 Version III
20
Notes: A typical double-hung window has numerous components. Understanding window terminology lets installers communicate effectively with each other when installing windows.
Head jamb  Groove at the top of the window that allows the window sashes to slide into place and sit inside the window frame.
Upper sash  The top portion of the window comprised of a pane of glass set inside a frame. The upper sash is fixed in a single-hung window and slides up and down in a double-hung window.
Glass pane  In the window shown in the slide, there are two panes of glass – one in the top sash and one in the bottom sash.
Side jamb  Grooves in window that allow the window sashes to slide up and down or side to side.
Trim  Extends beyond the end of the window frame on the outside of the window opening. This allows the window to fit flush with the exterior wall when the window is installed.
Window Stop  A wood trim member nailed to the window frame to hold, position, or separate window parts. The stop is often molded into the jamb liners on sliding windows.
Lower sash  The bottom portion of the window comprised of a pane of glass set inside a frame. The lower sash is fixed in a single-hung window and slides up and down in a double-hung window.
Sill  The very bottom of the window. The sill is usually sloped to allow water to run off the bottom of the window in rain or during cleaning.

## Slide 21: Window Types
Awning. Hopper has hinge on bottom
Picture or
Fixed
Casement
Slider
Double Hung
Image developed for US DOE WAP National Standardized Curricula
GJA 2024 Version III
21
Notes: The illustrations show several common window types.
Casement windows have a single operable sash that swings outward on a horizontal plane. Casement window frames that have gone out of square due to settling can stick and quite possibly render these types of windows inoperable.
Awning windows are essentially casement windows that swing vertically. Awning windows are often used in basements. Jalousie windows, found on older mobile homes, are a type of awning window.
Picture windows have no operable sashes and are used primarily for aesthetics.
Double-hung windows have operable upper and lower sashes that slide vertically in a channel. Upper sashes are often painted shut.
A slider window is essentially a double-hung window turned on its side so the sashes move horizontally.

## Slide 22: Window Treatments
Where applicable:
  Replace broken glass.
  Replace broken sash locks.
  Weatherstrip meeting rails and sliding surfaces.
  Install pulley seals.
  Caulk interior trim.
V-Channel
Stop
Upper Sash
Lower Sash
GJA 2024 Version III
22
Notes: Where applicable:
Replace broken glass.
Replace broken sash locks.
Weatherstrip meeting rails and sliding surfaces.
Install pulley seals.
Caulk interior trim.
Window repairs are usually simple but can be time consuming. Spending a great deal of time sealing every possible joint is not cost effective compared to fixing big duct leaks to the outside or large attic bypasses. However, air leakage around windows is noticeable to clients who sit near the windows during cold weather. Fixing these leaks will be appreciated.
Besides fixing obvious problems such as broken glass or misaligned sashes, very detailed window repairs such as weatherstripping, fixing broken sash locks, and caulking trim should be limited to high-activity areas where comfort is an issue.

## Slide 23
Glass Replacement
Remove broken pane.
Measure opening and cut new pane from glass sheet.
Install, point and glaze replacement pane.
Photo courtesy of the US Department of Energy
GENERAL CONSTRUCTION AND CARPENTRY
GJA 2024 Version III
23
Notes: When replacing glass, be sure to remove the broken pane. Next, measure the opening and cut a new pane from a glass sheet.
Important glazier tools:
Drywall square
Glass cutter
Wax crayon
Tape measure
Glaziers’ points
Putty knife
Safety glasses and gloves
Glazing compound

## Slide 24: Door Terminology
Hinge
Hinge Stile
Stop
Jamb
Casing
Threshold
Bottom Rail
Lock Rail
Lock Stile
Mullion
Top Rail
Panel
Image developed for US DOE WAP National Standardized Curricula
GJA 2024 Version III
24
Notes: This is an illustration of major door components:
Hinges: The metal objects that attach your door to the jamb, normally with screws. They can be made from brass, steel, iron, or other metals.
Door Casing: A wooden trim around doors that covers the seam between the jamb and the wall.
Jambs: The wood that surrounds the door unit to which the door is attached on the hinge side.
Door Stop: The wood trim fastened to the inside of the jamb that positions the door within the jamb and into the latching mechanism.
Threshold: A beveled wood member fastened to the floor and situated between the side jambs. The threshold seals the space between the bottom of the door and the floor.
On the door itself:
Rails: Horizontal framing members of a door.
Stiles: Full-length vertical framing members of a door.
Mullions: Vertical framing members that don’t run the full length of a door.
Panel: Parts of a door between the rails and stiles or mullions.

## Slide 25: Door Repair and Replacement
Sweep
Threshold
Replace doors only when :
    Favorable SIR.
    Or qualifies as incidental repair.
Apply weatherstripping, door stops, door sweeps, or thresholds.
Repair or replace locksets, deadbolts, latches, hinges.
Weatherization measures must have an SIR of at least 1.0.
Image developed for US DOE WAP National Standardized Curricula
GJA 2024 Version III
25
Notes: Replace doors only when:
    It is shown to have a favorable SIR.
    It can be justified as an incidental repair.
Apply weatherstripping, door stops, door sweeps, or thresholds. Repair or replace locksets, latches, and hinges.
Weatherization measures must have an SIR equal to or greater than 1 to be considered.

## Slide 26: Notes on Door Replacement
Replace door-only? Install solid wood or insulated door only if the rough opening is in good condition.
Consider pre-hung, energy-efficient door.
Site-built doors when possible, such as to bulkhead.
Employ lead-safe work practices.
GJA 2024 Version III
26
Notes: There are a couple of options for door replacement:
1) Replace the existing door with a solid core wood door blank.
Use this method only if the existing rough opening is reasonably square and the frame is in good shape.
This involves trimming a solid core door blank to fit, placing hinges, installing a lockset, weatherstripping, and priming.
A skilled carpenter with the right tools can install a door in about two hours.
Manufacture doors on site for special situations such as open coal access areas adjacent to conditioned basements.
Use lead-safe work practices when lead-based paint will be disturbed.
2) Install a pre-hung, energy-efficient unit that will fit the rough opening.
Consider installing a pre-hung unit if a commercially available unit will fit the rough opening.
This can be accomplished in much less time than retrofitting a door blank.
Use lead-safe work practices when lead-based paint will be disturbed.

## Slide 27: Summary
A good knowledge of residential construction terms helps for clear instructions on work orders.
Different framing styles require different strategies to seal air leaks.
Window and door replacements are generally not cost effective.
GJA 2024 Version III
27
Notes: A good knowledge of residential construction terminology helps auditors communicate clear instructions to crews and contractors.
Different framing configurations will require different strategies for controlling air leakage pathways.
Window and door replacements are generally not cost effective because they generally do not meet the minimum energy savings to investment ratio required by DOE.
Present this slide as an interactive discussion, soliciting personal examples from the trainees. Add your own personal examples and knowledge to supplement.