## Slide 1
CREW LEADER
Ongoing Training
1
GJA 2025 Version III
Notes: 1.7.2013
<number>
August 2012
‹#›

## Slide 2
By attending this session, participants will be able to:
    Explain basic adult learning theory.
    Discuss one-on-one training scenarios.
    Demonstrate group problem solving.
Learning Objectives
2
GJA 2025 Version III
Notes: 1.7.2013
By attending this session, participants will be able to:
Explain basic adult learning theory.
Discuss one-on-one training scenarios.
Demonstrate group problem solving.
<number>
August 2012
‹#›

## Slide 3
Requirements include:
    A trusting environment
    Mutual respect
    Freedom to experiment
    Pacing
    Active involvement
    Feedback
Adult Learning
3
GJA 2025 Version III
Notes: 1.7.2013
Requires:
A trusting environment – Establish a positive working environment in which everyone’s contribution is acknowledged and people feel comfortable sharing their concerns.
Mutual respect – Don’t talk down to crew members. Listen to them and respect their opinions. Remember that you don’t always have to be right! Compliment in public; reprove in private.
Freedom to experiment – Allow crew members to try new, reasonable methods and ideas.
Pacing – Too much information too quickly overwhelms; too little too slowly bores.
Active involvement – In a classroom, adult learners must have the opportunity to debate/discuss issues. Allow the same freedom at the job site.
Feedback – End every day with a recap of the day’s activities, positive and negative. Keep crew members informed of the results of in-house inspections and state monitoring so they know how they’re doing. If your agency gets a card or letter from a client commending your crew’s work, be sure they hear about it.
<number>
August 2012
‹#›

## Slide 4
At the Training Sight
Photo Source: US Department of Energy
Photo courtesy of the US Department of Energy
4
GJA 2025 Version III
Notes: 1.7.2013
When a trainer is brought in for on-the-job training, the crew leader should help the instructor keep everyone involved. In the picture here, at least two people in the foreground have their hands in their pockets. Be sure they grab the tube to blow the next floor cavity when this one is finished!
<number>
August 2012
‹#›

## Slide 5
Job Shadowing
5
GJA 2025 Version III
Notes: 1.7.2013
Job shadowingpairing a trainee to an experienced installercan provide an excellent learning experience.
As you assign trainees to experienced crew members, try to match similar personalities. More importantly, look for a positive attitude in the experienced person.
<number>
August 2012
‹#›

## Slide 6
Crew leader training responsibilities:
    Demonstrate new tasks.
    Assist new hires.
    Check work in progress.
    Encourage unmotivated workers.
    Provide feedback on completed tasks.
Day-to-Day Training
6
GJA 2025 Version III
Notes: 1.7.2013
The vast majority of weatherization installer training is on-the-job training (OJT).
The crew leader should:
Demonstrate all new tasks.
Assist new hires.
Check work in progress.
Encourage/motivate slackers.
Provide feedback on completed tasks.
<number>
August 2012
‹#›

## Slide 7
Demonstrate New Tasks
Photo Source: US Department of Energy
Dense-pack technique
Photo courtesy of the US Department of Energy
7
GJA 2025 Version III
Notes: 1.7.2013
Demonstrate proper methods for all new tasks.
The crew will respect and listen to a crew leader who demonstrates competence.
Always be willing to go anywhere you intend to send your crew members.
Be sure each crew member performs the task correctly at least once.
<number>
August 2012
‹#›

## Slide 8
Participate!
Photo courtesy of the US Department of Energy
8
GJA 2025 Version III
Notes: 1.7.2013
Don’t send your crew anywhere you would not go yourself!
<number>
August 2012
‹#›

## Slide 9
Assist New Hires
9
GJA 2025 Version III
Notes: 1.7.2013
Assist crew members who seem lost without embarrassing them.
Don’t do the task for trainees. Guide them through it.
Stay with trainees until you are sure they fully grasp and understand the task.
<number>
August 2012
‹#›

## Slide 10
Check Work in Progress
10
GJA 2025 Version III
Notes: 1.7.2013
Recommendations for checking work in progress include:
Do constant quality control.
Try to correct mistakes before they happen.
If something looks strange, ask questions before reproving. Your crew member may be trying an innovative approach that could have merit.
Learning is a two-way street.
A crew member developed the pictured method of attaching the strapping rail over the lower edge of the wall insulation to hold it in place rather than putting the strapping up first and then attaching the insulation to it.
<number>
August 2012
‹#›

## Slide 11
Observe Working Crew
11
GJA 2025 Version III
Notes: 1.7.2013
Stay in tune with the needs and progress of your crew by observing them at work.
<number>
August 2012
‹#›

## Slide 12
Motivate Slackers
12
GJA 2025 Version III
Notes: 1.7.2013
Keep everyone working. One unfocused, unproductive worker can demoralize an entire crew. The fellow sitting on the client’s deck isn’t contributing much!
<number>
August 2012
‹#›

## Slide 13
Provide Feedback on Completed Tasks
13
GJA 2025 Version III
Notes: 1.7.2013
Check major tasks as they are completed.
Make any necessary corrections at once.
Provide positive feedback to the installer when merited.
The picture shows an excellent whole house fan cover installation. Compliment the fabricator at break.
Q: Why at break?
A: Positive reinforcement is more effective if shared with peers.
<number>
August 2012
‹#›

## Slide 14
Don’t Forget Client Education
Follow the ground rules.
Show:
    Respect
    Understanding
    Honesty
14
GJA 2025 Version III
Notes: 1.7.2013
Your training responsibilities don’t end with your crew.
Successful client education has an extremely high savings-to-investment ratio (SIR). If a few moments of your time can convince a client to reduce energy use by a simple change in behavior, significant savings can be achieved at very little cost.
Explain how weatherization will change the operation of the home, any potential savings opportunities, and health and safety issues such as mold and mildew.
The same training principles apply when talking to clients as when training your crew.
Involve clients in the process as much as possible.
Try to spread important topics over time so you don’t overwhelm them.
Mention important points more than once. A good teacher introduces a point, discusses the point, and then summarizes it at the end.
Don’t talk down to clients or confuse them with trade jargon.
<number>
August 2012
‹#›

## Slide 15
Involve the Client!
15
GJA 2025 Version III
Notes: 1.7.2013
Having the client accompany you on your initial walk-through is an excellent way to establish credibility.
Most clients are very interested in any testing you perform during weatherization.
Explain the blower door, heating system efficiency test equipment, and infrared (IR) camera. Not only will clients better understand the workings of their home, they will also become ambassadors for weatherization with friends and relatives.
<number>
August 2012
‹#›

## Slide 16
Feel for Leaks
16
GJA 2025 Version III
Notes: 1.7.2013
The blower door is probably the most powerful educational tool we have.
In the home pictured, the crew chief is demonstrating to the client that a recently installed replacement door is still allowing large amounts of air to enter the home. If the client had that door replaced to reduce air leakage, it wasn’t worth it! Further demonstrating that the other doors and windows in the home do not leak under the same pressure can empower the client to make more informed replacement decisions in the future.
<number>
August 2012
‹#›

## Slide 17
Training Opportunities
(30 minutes)
Training Opportunities Exercise
17
GJA 2025 Version III
Notes: 1.7.2013
The following 18 slides are for use in the Training Opportunities Exercise. The listed responses may not be the only correct way to handle the pictured situation. Lead the class to logical conclusions in each instance.
<number>
August 2012
‹#›

## Slide 18
#1: Fogging
Heavy fogging occurs on inside of storm door glass after interior door is open for a few minutes.
18
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Moisture management – condensation on windows in a cold climate.
Target: Client
Method: Explain that whenever the dew point is exceeded, moisture will condense on hard surfaces. The condensation on window glass in a heating environment shows that the air contacting it is overly moist. Excessive moisture damages buildings and can cause health problems. If clients see condensation on windows on any but the coldest days, they should run exhaust fans until it goes away.
<number>
August 2012
‹#›

## Slide 19
#2: Chemicals Under Sink
During the blower door test, you find a number of highly caustic cleaners stored under the kitchen sink.
Photo courtesy of the US Department of Energy
19
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Indoor air quality (IAQ) and child safety – dangerous chemicals indoors.
Target: Client
Method: Explain that these products can off-gas and cause poor indoor air quality, which can lead to respiratory problems. Curious children can also ingest them, causing sickness or worse. Suggest that chemicals be stored in a safe place where small children can’t reach them. It’s best to store chemicals outside the home so they can’t off-gas into the living space.
<number>
August 2012
‹#›

## Slide 20
#3: Ladder by Bare Wires
You see this while checking on an attic blow-in progress
Photo courtesy of the US Department of Energy
20
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Safety – unbraced ladder on 6-mil. poly with bare wires nearby.
Target: Crew members
Method: Call an impromptu crew meeting. Explain OSHA workplace safety regulations. Brace the ladder against the left wall of the closet. Stop use of the drop cord.
<number>
August 2012
‹#›

## Slide 21
#4: Hose Reduction Fitting
This is noticed when crew is setting up to dense pack walls.
21
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Proper use of equipment – significant difference in blower hose sizes.
Target: Crew member assembling blower hose
Method: Explain that this type of shut-off/reducer was not designed for dense blow wall insulation. It will block repeatedly, slowing the job’s progress unless material flow is greatly reduced.
<number>
August 2012
‹#›

## Slide 22
Post and Beam
Your crew sees this from the van on the way to the job site.
#5: Post & Beam Barn Frame
22
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Good construction – observe post and beam framing details first hand.
Target: Crew members
Method: Stop for a few minutes. Ask the property owner for permission to inspect the frame. Raise awareness of necessary drill patterns for proper wall insulation and likely air sealing targets.
<number>
August 2012
‹#›

## Slide 23
#6: Vented Crawl Space
State monitoring visit
    Billed job
    Highly vented crawl space
23
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Fund source expectations – learn what the state monitor is looking for when inspecting weatherized buildings.
Target: Yourself. Remember you need training as well as your crew! Share any knowledge you gain with them.
Method: As your employer allows, either travel with the state monitor during a regular monitoring visit or arrange for the monitor to visit a job site where your crew is working.
Q: What do you think the state monitor will find here?
A: The poly ground cover is poorly sealed to the wall. The floor beneath the conditioned space is not insulated.
<number>
August 2012
‹#›

## Slide 24
#7: Crew Member in Attic
A crew member is observed crawling into the side attic to blow cellulose.
Photo courtesy of the US Department of Energy
24
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Safety – worker is not using personal protective equipment (PPE).
Target: Crew member
Method: Call the crew member down from the attic. Remind him of PPE rules. Be sure he is properly equipped before returning to the attic.
<number>
August 2012
‹#›

## Slide 25
This client says her windows are always greasy.
#8 Client Living Room
25
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: IAQ – overuse of candles.
Target: Client
Method: Explain to the client that burning candles often produces carbon monoxide (CO) and other contaminants. The greasiness on the windows is actually condensed candle wax. If the client will not agree to stop burning candles when windows are closed, encourage him/her to run an exhaust fan.
<number>
August 2012
‹#›

## Slide 26
#9: Dryer “Energy Saver”
    Checking on crawl space
    Ground cover materials in client utility room
Photo courtesy of the US Department of Energy
26
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: IAQ – Improper dryer venting.
Target: Client
Method: Explain to the client that excessive moisture and wash chemicals in the air can cause mold, which can lead to respiratory problems and damage the building. The crew will have to vent the dryer to the building exterior in order to insulate and air seal the home.
<number>
August 2012
‹#›

## Slide 27
#10: Slope IR
IR scan after slope blow is completed
27
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Proper installation technique and understanding of quality control methods – demonstrate the proper dense blow cellulose technique using an infrared scan.
Target: Dense blow crew
Method: Have the crew observe the IR pattern. Help the crew properly blow one or two bays. Repeat the IR and have the crew observe the pattern when the insulation is installed properly.
<number>
August 2012
‹#›

## Slide 28
#11: Gas Water Heater Pipe Wrap
New pipe wrap on gas water heater
Photo courtesy of the US Department of Energy
28
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Safety – failure to follow venting and fire code regulations.
Target: Installer
Method: Explain to the installer that flammable objects cannot be within three pipe diameters of the vent pipe—e.g., a 4 in. pipe requires 12 in. clearance. Have the installer remove the wrap and reinstall so the water pipe insulation is far enough from the vent pipe to meet code.
<number>
August 2012
‹#›

## Slide 29
#12: Plenum Insulation
Plenum insulation being installed
29
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Safety – failure to follow fire codes.
Target: Crew and the auditor if the work order didn’t call for a cleaning or tune up (clean/tune).
Method: Explain to the auditor and crew the significance of carbon particles at the furnace air intake (incomplete combustion and backdrafting).
<number>
August 2012
‹#›

## Slide 30
#13: Furnace Room
Furnace room: Cement block walls
Photo courtesy of the US Department of Energy
30
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Measure selection – insulated ducts and water pipes in conditioned space; R-3 box sills insulated while R-1 cement block walls untreated.
Target: Auditor and crew
Method: Explain that insulating ducts and pipes in a conditioned space has marginal, if any, SIR (no temperature difference (∆T)). Regarding the sills and walls, explain that DOE Rule 10 CFR 440 requires that tasks be done in order of the highest SIR first and that skipping over tasks is not allowed.
<number>
August 2012
‹#›

## Slide 31
#14: Work in Progress
Work in
progress
31
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Attention to detail – excellent job protecting client property.
Target: Crew
Method: At break, mention how much you appreciate the crew’s attention to detail in protecting the fireplace and walls while insulating and boarding over the exposed beam ceiling.
<number>
August 2012
‹#›

## Slide 32
#15: Attic Hatch
New attic
hatch
32
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Attention to detail – excellent job fabricating attic hatch that includes an insulation barrier, hooks and eyes, and nice trim.
Target: Crew
Method: At break, mention how much you appreciate the crew’s fine job of fabricating the attic hatch. You can also submit pictures and drawings crediting your crew to your state’s Best Practices file (if available). That’s a great motivator!
<number>
August 2012
‹#›

## Slide 33
#16: Attic Air Sealing
Attic air
sealing
33
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Proper air sealing methods – poor job air sealing an attic.
Target: Novice crew member
Method: Bring the trainee to the attic and demonstrate how to remove floorboards for access. Seal the partition top with one-part foam. Allow the trainee to proceed on his or her own. Check and critique the work once the job is done.
<number>
August 2012
‹#›

## Slide 34
#17: Chimney Chase
Chimney chase just
prior to blowing cellulose
Photo courtesy of the US Department of Energy
34
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Proper air sealing methods – missed bypass.
Target: Air sealing installer
Method: Check the area to be blown before starting cellulose installation. Show the installer the missed bypass. Explain to the installer that a blower door can easily detect a missed penetration even after it is buried in cellulose, requiring the installer to dig through the cellulose to seal the bypass properly. Have the installer complete the job correctly. Explain that there are consequences to not doing your job properly. If this oversight wasn’t found until the job was completed, it could cause a callback to seal the chase, wasting expensive production time. An employer should not tolerate such behavior very long.
<number>
August 2012
‹#›

## Slide 35
#18: Air Seal Check
Post cellulose air seal check
Photo courtesy of the US Department of Energy
35
GJA 2025 Version III
Notes: 1.7.2013
Training Opportunity: Proper air sealing methods – missing air sealing around wiring.
(This mistake was discovered after the task was completed. This is a serious problem. Either the installer is poorly trained or, worse, the person believed it was possible to skip an unpleasant task and not get caught.)
Target: Air sealing installer
Method: Bring the installer to the attic. Show him/her the missing air sealing at the wire. While you observe, have the installer dig up any other nearby pipe and wire penetrations or partition tops. If the others are properly air sealed, have the installer seal the missed area and complete the attic. If the other penetrations are not air sealed, require the installer to uncover and air seal all partition tops and wire penetrations in the attic.
Carefully check the work, either by visual inspection or with the blower door and pressure probe inserted into wall cavities before allowing the installer to proceed to another task. Warn the installer that you will be watching his or her work carefully for a period of time. A repeat offense is likely to cost the installer his or her job.
<number>
August 2012
‹#›

## Slide 36
ONGOING TRAINING
36
GJA 2025 Version III
Notes: 1.7.2013
Adult learning requires:
A safe environment.
Mutual respect.
Acceptance as an equal.
Freedom to experiment.
Pacing.
Active involvement.
Feedback.
<number>
August 2012
‹#›

## Slide 37
    Crew members generally learn best with one-on-one, hands-on training.
    Training should be an integral part of the workday.
    Give your crew constant feedback on their performance.
    Remember client education!
Summary
37
GJA 2025 Version III
Notes: 1.7.2013
Crew members generally learn best with one-on-one, hands-on training.
Training should be an integral part of the work day.
Give your crew constant feedback on their performance.
Remember to educate the client!
Present this slide as an interactive discussion, soliciting personal examples from the trainees. Add your own personal examples and knowledge to supplement.
<number>
August 2012
‹#›